## Slide 1
The Project
Hardware Design
E2.01- Ingram Readymix Secured Network
Ahmed Al Qaysi, Nicholas Holleman, Andres Oliva
Sponsor: Mr. Charlie Tuttle
Our project upgrades a remote retention pond with new hardware and software. This includes:
Power management
Blockchain ledger
Graphical user interface
Encryption (Security)
Remote Retention Pond Flow Chart
Motivation
Requirements & Results
Hardware
Acknowledgements
Dr. Stan McClellan
Mr. Mark Walker
Mr. Charlie Tuttle
The Ingram Readymix facility is under a TCEQ permit that requires the plant to report a water sample within 30 minutes when water leaves through a storm drain.
Hardware Implemented:
Microcontroller
RTC
Sleep Mode
LCD
Replace LED strip
Pass-Present data
Sensors
Battery life
Voltage
Current
Protection
Over-voltage shutdown
Under-voltage lockout
Network Communication
TCP
Encryption : RSA
I2C
Microcontroller management
Data Ledger
Block Chain
Error Handling
Sensors
Network
Power Subsystem
Features | Requirements | Data
Data Ledger | Verifiable data record. Store 3 years of records | Storage size: 1.85 Gbytes
Microcontroller
Microprocessor
Power Management | 3-day minimum battery life
Communication | Neglects unauthorized transmissions. | Retransmitted Blocks: 1.2% Time to Transmit: 1.02 seconds
Overall System | Samples sensor every 30 seconds. | 
Chart: Sensor Sample Cycle Times
| µ-Controller Cycle | µ-Processor Cycle Time | µ-Processor Cycle & Transmit
Seconds | 30 | 16.03 | 132.06
Both Devices are located in a IP65 rated box at the Pond.
Chart: Power Management Results
| No rain | Constant outflow | Old system
Power Consumption | 3.0343 | 62.3718 | 134.0647
Battery Life | 79.0947 | 3.8479 | 1.7902
Graphical User Interface | Display past and current water level, Battery life, 3 Clicks maximum to any location within GUI
Communication
I2C
UART
Power Management
Relay control